## Slide 1: Accelerating Genomic Sequence Alignment Workload with Scalable Vector Architecture
University of Michigan, Ann Arbor
Dong-hyeon Park, Jon Beaumont, Trevor Mudge

## Slide 2
“Human Genome Project”, 2004
Weeks
~$3 billion
~13 hours
<$10,000
Past
Present
“SpeedSeq”, 2015
DNA Storage
Portable Sequencer
Future Applications
Forensics
On-Demand
Diagnosis
source: National Institute of Health
Genomics
Human Genome:
3.2 billion base pairs
Need to sample at 30-50x coverage

## Slide 3
Read/Extract
Sequences
Reading fragment samples of whole genome
Signal/Image processing
Analysis
Identifying gene variants and abnormalities
Pattern matching, HMM, DNN
Sequence
Alignment
Matching overlaps across multiple sequences
Dynamic vs heuristic algorithm
reference gene
Assembly
Reconstructing the original sequence
de-novo vs mapping assembly
reconstructed
sequence
Whole Genome Sequencing Pipeline
10-20k in length

## Slide 4: Target Architecture:
Scalable Vector Extension (SVE)

## Slide 5
ARM’s Scalable Vector Extension (SVE)
Designed to complement existing SIMD architecture (NEON)
Key Features:
  Scalable Vector Length (128 - 2048-bits)
  Per-lane Predication (32 SIMD Reg. + 16 Predicate Reg.)
  Gather-load and scatter-store
  Horizontal vector operations
Vector Length Agnostic Code

## Slide 6
ARM’s Scalable Vector Extension (SVE)
Genomic sequences are sampled at different lengths depending on the device used for sampling:
  Illumina HiSeq System: 30-300 bps
  Sanger 3730xl: 400-900 bps
Vector-Length Agnostic Code can be used to Dynamically Choose the Optimal SIMD Width

## Slide 7: Target Algorithm:
Smith-Waterman
Sequence Alignment

## Slide 8
Smith-Waterman Algorithm
Local sequence alignment algorithm developed in 1981
Reference Sequence
Query Sequence
Inputs:
Output:
Alignment Location & Score
Scoring Matrix Construction
Matrix Backtracking
Smith-Waterman

## Slide 9
 | -- | A | C | A | C | A | A | 
-- | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 
A | 0 |  |  |  |  |  |  | 
G | 0 |  |  |  |  |  |  | 
C | 0 |  |  |  |  |  |  | 
A | 0 |  |  |  |  |  |  | 
…
…
…
…
…
…
…
…
…
Scoring
Scoring Matrix Construction
Reference Sequence
Query Sequence

## Slide 10
 | -- | A | C | A | C | A | A | 
-- | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 
A | 0 | 2 | 1 | 2 | 1 | 2 | 2 | 
G | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 
C | 0 | 0 |  |  | 3 | 2 | 1 | 
A | 0 | 2 |  | 5 |  |  |  | 
2
2
3
…
…
…
…
…
…
…
…
…
Reference Sequence
Query Sequence
Scoring
Scoring Matrix Construction

## Slide 11
 | -- | A | C | A | C | A | A | 
-- | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 
A | 0 | 2 | 1 | 2 | 1 | 2 | 2 | 
G | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 
C | 0 | 0 | 3 | 2 | 3 | 2 | 1 | 
A | 0 | 2 | 2 | 5 | 4 | 5 | 4 | 
C | 0 | 1 | 4 | 4 | 7 | 6 | 6 | 
max entry
1
Query Sequence
Reference Sequence
Backtracking
Backtracking
Finds the best local alignment from the scoring matrix
Step 2.
Check the adjacent entries for the next largest score
Move to the entry with the largest score and continue the path
Traverse back through the largest score
2

## Slide 12
 | -- | A | C | A | C | A | A | 
-- | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 
A | 0 | 2 | 1 | 2 | 1 | 2 | 2 | 
G | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 
C | 0 | 0 | 3 | 2 | 3 | 2 | 1 | 
A | 0 | 2 | 2 | 5 | 4 | 5 | 4 | 
C | 0 | 1 | 4 | 4 | 7 | 6 | 6 | 
max entry
1
Query Sequence
Reference Sequence
Backtracking
Backtracking
Finds the best local alignment from the scoring matrix
Traverse back through the largest score
2
Step 3.
Get the resulting alignment
Path Direction | Alignment
Horizontal | Deletion
Vertical | Insertion
Diagonal | Match

## Slide 13
 | -- | A | C | A | C | A | A | 
-- | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 
A | 0 | 2 | 1 | 2 | 1 | 2 | 2 | 
G | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 
C | 0 | 0 | 3 | 2 | 3 | 2 | 1 | 
A | 0 | 2 | 2 | 5 | 4 | 5 | 4 | 
C | 0 | 1 | 4 | 4 | 7 | 6 | 6 | 
max entry
1
Query Sequence
Reference Sequence
Backtracking
Backtracking
Finds the best local alignment from the scoring matrix
Traverse back through the largest score
2
Step 3.
Get the resulting alignment
3
Reference: A-CAC
Query: AGCAC
Insertion
Alignment Score: 7

## Slide 14
Reference
Query
L
L
Alignment Location & Score
Vectorization
[0]
[1]
[2]
[3]
Wavefront:
[2] Wozniak et al
[3] Farrar
[4] Rognes
(striped)

## Slide 15
Batch Smith-Waterman
Reference Sequence
Query Sequences Sampled
 | 0 | 0 | 0 | 0 | 0
Query 0
Reference 0
SVE[0]
 | 0 | 0 | 0 | 0 | 0
Query 1
Reference 1
SVE[1]
 | 0 | 0 | 0 | 0 | 0
Query K
Reference K
SVE[K]
…
…
[4] Rognes

## Slide 16
 | -- | A | C | A | C | A | G | T | A | C | A | 
-- |  |  |  |  |  |  |  |  |  |  |  | 
A |  |  |  |  |  |  |  |  |  |  |  | 
G |  |  |  |  |  |  |  |  |  |  |  | 
C |  |  |  |  |  |  |  |  |  |  |  | 
A |  |  |  |  |  |  |  |  |  |  |  | 
…
…
…
…
…
…
…
…
Reference Sequence
Query Sequence
Sliced Smith-Waterman
…
…
…
…
…
…
…
…
…
…
VL = K
SVE[0]
SVE[1]
SVE[K-1]
SVE[0]
SVE[1]
SVE[2]
1
E
H
F
Initial Calculation of H(m,n)
[3] Farrar
(striped)

## Slide 17
 | -- | A | C | A | C | A | G | T | A | C | A | 
-- |  |  |  |  |  |  |  |  |  |  |  | 
A |  |  |  |  |  |  |  |  |  |  |  | 
G |  |  |  |  |  |  |  |  |  |  |  | 
C |  |  |  |  |  |  |  |  |  |  |  | 
A |  |  |  |  |  |  |  |  |  |  |  | 
…
…
…
…
…
…
…
…
Reference Sequence
Query Sequence
Sliced Smith-Waterman
…
…
…
…
…
…
…
…
…
…
VL = K
SVE[0]
SVE[1]
SVE[K-1]
SVE[0]
SVE[1]
SVE[2]
1
horizontal dependencies
between slices not accounted
E
H
F
Value of F need to be re-calculated
[3] Farrar
(striped)

## Slide 18
 | -- | A | C | A | C | A | G | T | A | C | A | 
-- |  |  |  |  |  |  |  |  |  |  |  | 
A |  |  |  |  |  |  |  |  |  |  |  | 
G |  |  |  |  |  |  |  |  |  |  |  | 
C |  |  |  |  |  |  |  |  |  |  |  | 
A |  |  |  |  |  |  |  |  |  |  |  | 
…
…
…
…
…
…
…
…
Reference Sequence
Query Sequence
Sliced Smith-Waterman
…
…
…
…
…
…
…
…
…
…
VL = K
SVE[0]
SVE[1]
SVE[K-1]
SVE[0]
SVE[1]
SVE[2]
Resolve Dependencies
2
F
F
[3] Farrar
(striped)

## Slide 19
Wavefront Smith-Waterman
E
H
F
All dependency comes from previous execution
 | -- | A | C | A | C | A | G | T | A | C | A | 
-- |  |  |  |  |  |  |  |  |  |  |  | 
A |  |  |  |  |  |  |  |  |  |  |  | 
G |  |  |  |  |  |  |  |  |  |  |  | 
C |  |  |  |  |  |  |  |  |  |  |  | 
A |  |  |  |  |  |  |  |  |  |  |  | 
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
1
0
F,E
Reference Sequence
Query Sequence

## Slide 20
Wavefront Smith-Waterman
E
H
F
All dependency comes from previous execution
 | -- | A | C | A | C | A | G | T | A | C | A | 
-- | H |  |  |  |  |  |  |  |  |  |  | 
A |  |  |  |  |  |  |  |  |  |  |  | 
G |  |  |  |  |  |  |  |  |  |  |  | 
C |  |  |  |  |  |  |  |  |  |  |  | 
A |  |  |  |  |  |  |  |  |  |  |  | 
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
1
2
0
F,E
F,E
Reference Sequence
Query Sequence
[2] Wozniak et al

## Slide 21
Wavefront Smith-Waterman
E
H
F
All dependency comes from previous execution
 | -- | A | C | A | C | A | G | T | A | C | A | 
-- |  | H |  |  |  |  |  |  |  |  |  | 
A | H |  |  |  |  |  |  |  |  |  |  | 
G |  |  |  |  |  |  |  |  |  |  |  | 
C |  |  |  |  |  |  |  |  |  |  |  | 
A |  |  |  |  |  |  |  |  |  |  |  | 
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
1
2
0
3
F,E
F,E
F,E
Reference Sequence
Query Sequence
[2] Wozniak et al

## Slide 22
Wavefront Smith-Waterman
E
H
F
All dependency comes from previous execution
 | -- | A | C | A | C | A | G | T | A | C | A | 
-- |  |  |  |  |  |  |  |  |  |  |  | 
A |  |  |  |  |  |  |  |  |  |  |  | 
G |  |  |  |  |  |  |  |  |  |  |  | 
C |  |  |  |  |  |  |  |  |  |  |  | 
A |  |  |  |  |  |  |  |  |  |  |  | 
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
1
2
0
4
3
F
F,E
F,E
F,E
F,E
H
H
H
H
Reference Sequence
Query Sequence
More book-keeping overhead than other algorithms:
Keep track of H values of two prev. iterations
F and E values from prev. iteration
[2] Wozniak et al

## Slide 23: Experimental Evaluation:
Smith-Waterman on gem5 w/ SVE

## Slide 24
Experimental Setup
Gem5 Simulator w/ ARM SVE Simulation

## Slide 25
Experimental Setup
Application:
Smith-Waterman – Batch, Sliced, and Wavefront
Reference :
  25-400 bps samples from E. Coli 536 Gene (4.9 Mbps)
Query :
  1000 x 25-400 bps samples through WGSim

## Slide 26
Advantage of SVE over Traditional System
CPU, NEON implementation written in C. SVE hand-written in assembly.
SVE outperforms both CPU and NEON implementations by at least 3x
Batch, Sliced and Wavefront used 32-bit, 16-bit and 64-bit vectors respectively.
Chart: Alignment Time Speedup over Baseline CPU
| 25 | 50 | 100 | 200 | 400
cpu | 1 | 1 | 1 | 1 | 1
batch_neon | 1.5227 | 1.5131 | 1.4231 | 1.3637 | 1.3425
sliced_neon | 0.16261 | 0.43863 | 0.82724 | 1.4017 | 2.0636
batch_sve_128bit | 10.8398 | 9.6679 | 8.237 | 7.7828 | 7.4511
sliced_sve_128bit | 3.2583 | 8.9988 | 16.7226 | 28.08 | 38.1659
wavefront_128bit | 2.5595 | 6.9325 | 5.6307 | 5.2374 | 5.5548

## Slide 27
Impact of Handwritten Assembly
Chart: Speedup of Wavefront Algorithm
| L=25 | L=50 | L=100 | L=200
CPU (naïve) | 1.8478 | 1.2463 | 1.5949 | 1.6886
CPU (wav) | 1 | 1 | 1 | 1
CPU-ASSEM | 3.8159 | 5.7675 | 5.0874 | 5.3795
SVE-128bit | 4.7295 | 8.6399 | 8.9803 | 9.2435
SVE-256bit | 6.1458 | 11.9136 | 14.3395 | 15.9487
Hand-written assembly code of Wavefront Algorithm has 4-6x speedup over C code.

## Slide 28
Advantage of SVE over Traditional System
SVE reduces the instruction execution significantly compared to CPU or NEON
Chart: Instructions Executed Compared to Baseline CPU
| 25 | 50 | 100 | 200 | 400
cpu | 1 | 1 | 1 | 1 | 1
batch_neon | 0.61576 | 0.47796 | 0.45258 | 0.45287 | 0.45961
batch_sve_128bit | 0.45015 | 0.25329 | 0.18444 | 0.15956 | 0.15573
sliced_neon | 2.2061 | 1.0495 | 0.57835 | 0.31596 | 0.23926
sliced_sve_128bit | 0.21731 | 0.10541 | 0.065876 | 0.042633 | 0.034199
wavefront_128bit | 0.27107 | 0.13692 | 0.19982 | 0.21713 | 0.20987

## Slide 29
Chart: Memory Bandwidth of Batch S-W: SVE 512-bit, 64kB L1D
| L025 | L050 | L100 | L200 | L400
read_bw | 11.7456 | 12.6807 | 15.5979 | 458.5995 | 4351.1917
write_bw | 9.3046 | 10.9305 | 13.9911 | 383.3471 | 569.4723
Chart: Memory Bandwidth of Sliced S-W: SVE 512-bit, 64kB L1D
| L025 | L050 | L100 | L200 | L400
read_bw | 16.7099 | 8.8419 | 2.9603 | 1.4907 | 1.28
write_bw | 0.001298 | 0.00072 | 0.000268 | 0.000148 | 0.000126
Chart: Memory Bandwidth of Wavefront S-W: SVE 512-bit, 64kB L1D
| L025 | L050 | L100 | L200 | L400
read_bw | 98.1295 | 103.3277 | 32.5984 | 11.5695 | 2.5134
write_bw | 0.001975 | 0.00151 | 0.052502 | 0.093285 | 0.014358
Memory Bandwidth Comparison
Sliced and Wavefront significantly reduce the memory bandwidth compared to the Batch algorithm

## Slide 30
Vector Scaling of Different Algorithms
Chart: Vector Performance Scaling of Batch, Sliced, and Wavefront at Sequence Length of L=100
| 128-bit | 256-bit | 512-bit | 1024-bit
Batch | 1 | 0.99295 | 1.0013 | 0.95748
Sliced | 1 | 0.72169 | 0.42952 | 0.22782
Wavefront | 1 | 1.5968 | 2.413 | 2.5856
Chart: Vector Performance Scaling of Batch, Sliced and Wavefront at Sequence Length of L=400
| 128-bit | 256-bit | 512-bit | 1024-bit
Batch | 1 | 0.95564 | 0.89849 | 0.84064
Sliced | 1 | 1.4127 | 1.2609 | 0.28065
Wavefront | 1 | 1.7696 | 3.0219 | 3.3193
Batch and Sliced show marginal improvement with increasing vector length
Difficult to keep up with increased memory demand
Need to resolve dependencies.

## Slide 31
Chart: Comparison of Different Smith-Waterman Vectorization 512-bit SVE and 64kB L1D Cache
| 25 | 50 | 100 | 200 | 400
Batch | 8.3915 | 33.8884 | 129.7502 | 524.2619 | 2275.0187
Sliced | 30.7989 | 55.508 | 148.9955 | 269.9672 | 316.4953
Waveform | 20.2449 | 26.4766 | 78.7661 | 255.6353 | 1014.6498
Waveform
Sliced
Batch
Fixed HW Options: Batch vs Sliced vs Waveform @512-bit
Batch
Low overhead.
Poor scaling.
Fastest for short seq.
Waveform
Efficient use of vector Lanes
Fastest for medium seq.
Sliced
High overhead.
Execution bypassing
Fastest for long seq.

## Slide 32
HW with Variable Vector Length
Given freedom to choose the hardware for each sequence length, we can establish a set of optimal algorithm-hardware pair.
Read Length | Algorithm | Vector Length | Speedup Over 512-bit Wavefront
< 50 bps | Batch | 128-bit | 2.77
50-100 bps | Wavefront | 1024-bit | 1.03
100-400 bps | Sliced | 256-bit | 1.23-3.06
Notes: Negative results?
Explored PIM, but not looking good.

## Slide 33
Conclusion
Smith-Waterman on SVE:
+ Select Optimal Vector Length & Algorithm depending on Input
+ Lower Instruction Footprint
Improvements to memory controller can lead to improved performance
Wavefront algorithm use 64-bit vectors due to limitations on gather-scatter instruction addressing.
Notes: Negative results?
Explored PIM, but not looking good.

## Slide 34
Key References
[1] Smith TF, Waterman MS, “Identification of common molecular subsequences” J Mol Biol 147
[2] Wozniak A. “Using video-oriented instructions to speed up sequence comparison” Comput Appl Biosci. 1997
[3] Farrar M, “Striped Smith-Waterman speeds database searches six times over other SIMD implementations” Bioinformatics, Vol 23, Issue 2, 15 January 2007
[4] Rognes T, “Faster Smith-Waterman database searches with inter-sequence SIMD parallelization” Bioinformatics 2011
[5] Zhao M, Lee W, Garrison E., Marth G. “SSW Library: An SIMD Smith-Waterman C/C++ Library for Use in Genomic Applications”
[6] Li H, Durbin R. “Fast and accurate short read alignment with Burrows-Wheeler transform” Bioinformatics 25
[7] Steinfadt S. “SWAMPT+: Enhanced Smith-Waterman Search for Parallel Models”

## Slide 35: Questions?